## Slide 1
RAPTOR-SoC Architecture
CPU-controlled SIMT GPU with AXI4-Lite control and shared memory
CLOCK + RESET
Single shared domain
CPU SIDE
GPU SIDE
RISC-V CPU
Multi-cycle RV32I
Private instruction TCM
ADDI | LW | SW
BEQ | BNE | JAL
AXI4-Lite Interconnect
32-bit control + data
Round-robin arbitration
Address decode
GPU MMIO
CTRL | STATUS
THREADS | SRC
DST | PROG_BASE
SIMT GPU
2 warps x 4 lanes
8 physical threads
DCR | dispatcher
16-bit custom ISA
Shared RAM
32K x 32 dual-port | host + pixel ports
Framebuffer A (src) 0x2000
Framebuffer B (dst) 0x6000
GPU Program Memory
1024 x 16-bit
Blur kernel
Brighten kernel
CPU AXI master
AXI MMIO
AXI RAM host port
GPU control
GPU pixel bus
(word addressed)
Instruction fetch
Blue: AXI4-Lite | Purple: GPU control | Green: pixel data | Gray: private fetch and clock